Instuction for Power Distribution Board

- Main parts of the Power Distribution Board as below,

- Main board

- Adjustable voltage outpur part for 10V-20V, maximum output power:36W, 12V output 3A

- Regulated voltage output for 5V, maximum power:15W,  5V output 3A

- Assemble diagram as follow,

As the picture shows, solder the power module with main board with matched pin. It has labels on the installation modules of the main board, and with fool-proofing design, if wrongly install the module, the soldering hole will be not matched.

3. Input/output disgram,

Mark 1 and Mark 2 both are the power input(VIN/VOUT is positive, GND is negative).

Mark 3 is regulated voltage output for 5V( label 5V is positive, GND is negative, which can output 4 channels power at the same time).

Mark 4 is adjustable voltage output for 10V-20V(label 10V is positive, GND is negative, which can output 4 channels power at the same time).

Mark 5 is the power output, it is to connect ESC or other equipments, each solderred pad has the screen printing label “ +/- ”,  label “ + ” is positive, label “ - ” is negative.

Note: The LED of the main board need to be supported by module 5V, it will be lit after finished assembled.

Basic parameter of the power distribution board:

Assembling hole:45X45MM

Thickness of copper-coated: 4OZ

Discharge capacity of motor circuit:6S 120A

Output power for module 5V: 15W

Output power for variable voltage 10-20V: 36W
buy link:

http://www.thanksbuyer.com/j-and-k-dual-bec-esc-power-distribution-board-power-connection-plate-with-led-100a-for-multirotor-28984
welcome to thanksbuyer.com